## Slide 1: Computer Networks Fall 2023
Programing Assignment
3. Transport Layer Assignment
Hou Huawei
1136288430@qq.com
Zhixin Building N201

## Slide 2: Assignment 1 Stop-and-wait
In this assignment, you will develop a “Stop-and-wait” protocol in Python(Socket). You should write a server and a client.
(1) Your client will send a message to server and wait ack from server. If timeout, client should resend message.
(2) Your server will receive message from client and return an ack to it.
(3) In real world tranfer process, packet loss is not recurrent, so that you should manually set a loss mechanism in your server.
(4) Packet number should can be define freely
(5) After all packets have been sent, client counts packet loss rate and time spent, which contains average RTT of every packet and total time.

## Slide 3: 任务1 停等协议
在这个任务中，您将使用Python（Socket）开发一个“停等”协议。您需要编写一个服务器和一个客户端。
（1）您的客户端将向服务器发送消息并等待来自服务器的确认。如果超时，客户端应重新发送消息。
（2）您的服务器将从客户端接收消息并向其返回确认。
（3）在真实的传输过程中，数据包丢失不是经常发生的，因此您应该在服务器中手动设置一个丢包机制。
（4）数据包编号应该可以自由定义。
（5）在所有数据包发送完毕后，客户端计算数据包丢失率和时间消耗，其中包括每个数据包的平均往返时间（RTT）和总时间。

## Slide 4: Server 服务器
(1) Creating TCP/UDP socket
(2) Receiving data from client
(3) Return Ack, you can define an Ack manually
(1) 创建TCP/UDP套接字
(2) 从客户端接收数据
(3) 返回确认，您可以手动定义确认信息（Ack）

## Slide 5: Client
(1) Creating TCP/UDP socket
(2) Sending a series of packet to server, and the number of packet can be assigned
(3) Receiving Ack from server and counting
(4) Setting a timeout
(5) If timeout, the packet should resend packet
(6) After all packet are sent, print time and paket loss rate

## Slide 6: 客户端
(1) 创建TCP/UDP套接字
(2) 向服务器发送一系列数据包，可以指定数据包的数量
(3) 从服务器接收确认信息并计数
(4) 设置超时时间
(5) 如果超时，应重新发送数据包
(6) 在所有数据包发送后，打印时间和数据包丢失率

## Slide 7: Advise
(1) Using loop statement to set how many packet .
(2) Set a packet loss mechanism manually:
Similar to former “udp pinger”, you can generate random number through “random” series function.
(3) Counting RTT:
Using “datetime” and “statistics” module.

## Slide 8: 建议
(1) 使用循环语句设置数据包的数量。
(2) 手动设置数据包丢失机制：
类似于以前的“UDP Pinger”，您可以通过“random”系列函数生成随机数。
(3) 计算往返时间（RTT）：
使用“datetime”和“statistics”模块。

## Slide 9: Content
(1) communication in “localhost”
----① Sending 10 packets, packet loss rate is set to 0.5
----② Sending 100 packets, packet loss rate is set to 0.2
----③ Sending 100 packets, packet loss rate is set to 0.5
(2) communication with your partner
----same as (1)

## Slide 10: 内容
(1) 在“localhost”中的通信
----① 发送10个数据包，数据包丢失率设置为0.5
----② 发送100个数据包，数据包丢失率设置为0.2
----③ 发送100个数据包，数据包丢失率设置为0.5
(2) 与您的合作伙伴进行通信
----与（1）相同

## Slide 11: Demo

## Slide 12: The files you need to upload
You should upload ZIP file, which contains the following files:
① StopAndWait_server.py
② StopAndWait_client.py
③ report file
Deadline: November 26, 2023

## Slide 13: About report
(1) Work in groups to complete the lab report in English or Chinese.
(2) Do not append code to report.
(3) Need not rich contents, just explain your assignment concisely.
(1) 分组完成实验报告，可以使用英语或中文。
(2) 不要将代码附加到报告中。
(3) 无需过多的内容，简洁地解释您的任务即可。

## Slide 14: Standard for Evaluation
(1) Uploading file before deadline
(2) Whether the task has been completed --40%
(3) Comments in the code (in Chinese) --30%
(4) Clear and concise report --30%
*Report should be written in English

## Slide 15: 实验报告标准
(1) 在截止日期前上传文件
(2) 任务是否已完成 —— 40%
(3) 代码中的注释（中文） —— 30%
(4) 报告清晰而简洁 —— 30%
*报告应以英语撰写。